## Slide 1: M2
Zeduo Yu Pengyang Zhou Xiwei Wang
zeduoyu2 pz6 xiwei2
ECE411 MP4 Demonstration

## Slide 2: Overview
Out-of-order CPU with Reorder Buffer.
A branch predictor utilizing local branch history table and return address stack.

## Slide 3: Feature 1, Out-of-order Execution.
Diagram >

## Slide 4: Feature 1, Out-of-order Execution.
Reservation Station Definition >

## Slide 5: Feature 1, Out-of-order Execution.
Challenges >
1. CDB complexity.
2. Fitting the design.
3. Edge case timing.
4. Debug difficulty.
😭
Notes: flush timing. register read and write.

## Slide 6: Feature 2, Branch Predictor.
Diagram >
BR type

## Slide 7: Feature 2, Branch Predictor.
Diagram >
JALR type

## Slide 8: Feature 2, Branch Predictor.
Performance >
Accuracy1 | Comp1 | Comp2_i | Comp3
Our design | 89.52% | 84.39% | 89.12%
1. Include JAL/JALR operations.

## Slide 9: Feature 2, Branch Predictor.
Challenges >
1. Critical path.
2. JALR handling.

## Slide 10: Overall Performance
4.1x
Up to
faster execution speed1
1. Compared to baseline implementation
Time/ns | Comp1 | Comp2_i | Comp3
Our design | 702,920 | 3,040,950 | 894,860
Baseline | 720,755 | 4,521,285 | 3,639,265
MP2 | 14,563,465 | 28,469,605 | 17,763,205

## Slide 11: Overall Performance
Power/mw | Comp1 | Comp2_i | Comp3
Our design | 979.21 | 949.26 | 960.27
Baseline | 448.44 | 430.48 | 425.27
2x
But about
More power consumption

## Slide 12: Overall Performance
Score1 | Comp1 | Comp2_i | Comp3
Our design | 3.10E-10 | 2.44E-8 | 6.28E-10
Baseline | 1.68E-10 | 3.98E-8 | 2.05E-8
32x
Up to
faster execution speed2
Use Fmax = 103.11MHz of model “Slow 900mV 100C”
Compared to baseline.

## Slide 13: Competition Score
Gem Mean = (3.10E-10 x 2.44E-8 x 6.28E-10)^(1/3)
1.681E-9
That is better than the baseline score (5.15E-09).
3.1x

## Slide 14: What if…
Superscalar? Put more demand on instruction cache and resources. But a chance to achieve higher performance.
L2 cache? May provide higher hit rate. But our caches are good enough.
Non-blocking cache? Requires tremendous effort and resources. Would try it if more time was given.
Simultaneous commit? Commit multiple instructions at the same time. Too much complexity.

## Slide 15: Q&A
Thank you for listening.